## Slide 1
Dr. Rizwan Khan
Head – Department of Computer Science and Engineering
(An NBA Accredited Program)
ABES Institute of Technology, Ghaziabad
COMPUTER ORGANIZATION AND ARCHITECTURE

## Slide 2: MEMORY ORGANIZATION
Memory Hierarchy
Main Memory
Cache Memory
Virtual Memory

## Slide 3: MEMORY HIERARCHY
Magnetic
tapes
Magnetic
disks
I/O
processor
CPU
Main
memory
Cache
memory
Auxiliary memory
Register
Cache
Main Memory
Magnetic Disk
Magnetic Tape
Memory Hierarchy is to obtain the highest possible
access speed while minimizing the total cost of the memory system
Memory Hierarchy

## Slide 4: Characteristics
Location
Capacity
Unit of transfer
Access method
Performance
Physical type
Physical characteristics
Organisation

## Slide 5: Location
CPU
Internal
External

## Slide 6: Capacity
Word size
  The natural unit of organisation
Number of words
  or Bytes

## Slide 7: Unit of Transfer
Internal
  Usually governed by data bus width
External
  Usually a block which is much larger than a word
Addressable unit
  Smallest location which can be uniquely addressed
  Word internally
  Cluster on M$ disks

## Slide 8: Access Methods (1)
Sequential
  Start at the beginning and read through in order
  Access time depends on location of data and previous location
  e.g. tape
Direct
  Individual blocks have unique address
  Access is by jumping to vicinity plus sequential search
  Access time depends on location and previous location
  e.g. disk

## Slide 9: Access Methods (2)
Random
  Individual addresses identify locations exactly
  Access time is independent of location or previous access
  e.g. RAM
Associative
  Data is located by a comparison with contents of a portion of the store
  Access time is independent of location or previous access
  e.g. cache

## Slide 10: Memory Hierarchy
Registers
  In CPU
Internal or Main memory
  May include one or more levels of cache
  “RAM”
External memory
  Backing store

## Slide 11: Memory Hierarchy

## Slide 12: Performance
Access time
  Time between presenting the address and getting the valid data
Memory Cycle time
  Time may be required for the memory to “recover” before next access
  Cycle time is access + recovery
Transfer Rate
  Rate at which data can be moved

## Slide 13: Physical Types
Semiconductor
  RAM
Magnetic
  Disk & Tape
Optical
  CD & DVD
Others
  Bubble
  Hologram

## Slide 14: Physical Characteristics
Decay
Volatility
Erasable
Power consumption

## Slide 15: Organisation
Physical arrangement of bits into words
Not always obvious
e.g. interleaved

## Slide 16: Semiconductor Memory Types

## Slide 17: Semiconductor Memory
RAM
  Misnamed as all semiconductor memory is random access
  Read/Write
  Volatile
  Temporary storage
  Static or dynamic

## Slide 18: Read Only Memory (ROM)
Permanent storage
  Nonvolatile
Microprogramming (see later)
Library subroutines
Systems programs (BIOS)
Function tables