## Slide 1
Dr. Rizwan Khan
Head – Department of Computer Science and Engineering
(An NBA Accredited Program)
ABES Institute of Technology, Ghaziabad
COMPUTER ORGANIZATION AND ARCHITECTURE

## Slide 2: Types of ROM
Written during manufacture
  Very expensive for small runs
Programmable (once)
  PROM
  Needs special equipment to program
Read “mostly”
  Erasable Programmable (EPROM)
    Erased by UV
  Electrically Erasable (EEPROM)
    Takes much longer to write than read
  Flash memory
    Erase whole memory electrically

## Slide 3: MAIN MEMORY
RAM and ROM Chips
Typical RAM chip
Typical ROM chip
Chip select 1
Chip select 2
Read
Write
7-bit address
CS1
CS2
RD
WR
AD 7
128 x 8
RAM
8-bit data bus
CS1 CS2 RD WR
0 0 x x
0 1 x x
1 0 0 0
1 0 0 1
1 0 1 x
1 1 x x
Memory function
Inhibit
Inhibit
Inhibit
Write
Read
Inhibit
State of data bus
High-impedence
High-impedence
High-impedence
Input data to RAM
Output data from RAM
High-impedence
Chip select 1
Chip select 2
9-bit address
CS1
CS2
AD 9
512 x 8
ROM
8-bit data bus
Main Memory

## Slide 4: Random Access Memory (RAM)
Sequential circuits all depend upon the presence of memory.
  A flip-flop can store one bit of information.
  A register can store a single “word,” typically 32-64 bits.
Random access memory, or RAM, allows us to store even larger amounts of data. Today we’ll see:
  The basic interface to memory.
  How you can implement static RAM chips hierarchically.
This is the last piece we need to put together a computer!

## Slide 5: Introduction to RAM
Random-access memory, or RAM, provides large quantities of temporary storage in a computer system.
Remember the basic capabilities of a memory:
  It should be able to store a value.
  You should be able to read the value that was saved.
  You should be able to change the stored value.
A RAM is similar, except that it can store many values.
  An address will specify which memory value we’re interested in.
  Each value can be a multiple-bit word (e.g., 32 bits).
We’ll refine the memory properties as follows:
A RAM should be able to:
  - Store many words, one per address
  - Read the word that was saved at a particular address
  - Change the word that’s saved at a particular address

## Slide 6: Picture of memory
You can think of computer memory as being one big array of data.
  The address serves as an array index.
  Each address refers to one word of data.
You can read or modify the data at any given memory address, just like you can read or modify the contents of an array at any given index.
If you’ve worked with pointers in C or C++, then you’ve already worked with memory addresses.

## Slide 7: Block diagram of RAM
This block diagram introduces the main interface to RAM.
  A Chip Select, CS, enables or disables the RAM.
  ADRS specifies the address or location to read from or write to.
  WR selects between reading from or writing to the memory.
    To read from memory, WR should be set to 0.
    OUT will be the n-bit value stored at ADRS.
    To write to memory, we set WR = 1.
    DATA is the n-bit value to save in memory.
This interface makes it easy to combine RAMs together, as we’ll see.
2k x n memory
ADRS OUT
DATA CS
WR
k
n
n

## Slide 8: Memory sizes
We refer to this as a 2k x n memory.
  There are k address lines, which can specify one of 2k addresses.
  Each address contains an n-bit word.
For example, a 224 x 16 RAM contains 224 = 16M words, each 16 bits long.
  The RAM would need 24 address lines.
  The total storage capacity is 224 x 16 = 228 bits.
2k x n memory
ADRS OUT
DATA
CS
WR
k
n
n

## Slide 9: Typical memory sizes
Some typical memory capacities:
  PCs usually come with 512MB – 2GB RAM.
  PDAs have 16-64MB of memory.
  Digital cameras and MP3 players can have 32MB-8GB or more of onboard storage.
Many operating systems implement virtual memory, which makes the memory seem larger than it really is.
  Most systems allow up to 32-bit addresses. This works out to 232, or about four billion, different possible addresses.
  With a data size of one byte, the result is apparently a 4GB memory!
  The operating system uses hard disk space as a substitute for “real” memory.

## Slide 10: Reading RAM
To read from this RAM, the controlling circuit must:
  Enable the chip by ensuring CS = 1.
  Select the read operation, by setting WR = 0.
  Send the desired address to the ADRS input.
  The contents of that address appear on OUT after a little while.
Notice that the DATA input is unused for read operations.
2k x n memory
ADRS OUT
DATA
CS
WR
k
n
n

## Slide 11: Writing RAM
To write to this RAM, you need to:
  Enable the chip by setting CS = 1.
  Select the write operation, by setting WR = 1.
  Send the desired address to the ADRS input.
  Send the word to store to the DATA input.
The output OUT is not needed for memory write operations.
2k x n memory
ADRS OUT
DATA CS
WR
k
n
n