## Slide 1
Dr. Rizwan Khan
Head – Department of Computer Science and Engineering
(An NBA Accredited Program)
ABES Institute of Technology, Ghaziabad
COMPUTER ORGANIZATION AND ARCHITECTURE

## Slide 2: REPLACEMENT POLICIES
LRU
  the cache block that has been recently used the least is selected for replacement
LFU
  replaces the block in the set that has been referenced the least number of times.
  Implementation of LFU requires a counter associated with each cache line.
FIFO
  replaces the block that has been in the set for the longest time.
  FIFO policy can be implemented using a circular buffer.
RANDOM
  random selection of a cache block for replacement is done based on the output of the random number generator at the time of replacement.
  This technique is simple and does not require much additional overhead
OPTIMAL
  The optimal replacement policy is not practical, but is used for comparison purposes to determine how effective other replacement policies are to the best possible.
  The optimal replacement policy is determined only after a program has already executed, and so it is of little help to a running program