## Slide 1
Dr. Rizwan Khan
Head – Department of Computer Science and Engineering
(An NBA Accredited Program)
ABES Institute of Technology, Ghaziabad
COMPUTER ORGANIZATION AND ARCHITECTURE

## Slide 2: INPUT-OUTPUT ORGANIZATION
Peripheral Devices
Input-Output Interface
Asynchronous Data Transfer
Modes of Transfer
Priority Interrupt
Direct Memory Access
Input-Output Processor
Serial Communication

## Slide 3: PERIPHERAL DEVICES
Input Devices
Keyboard
Optical input devices
- Card Reader
- Paper Tape Reader
- Bar code reader
- Digitizer
- Optical Mark Reader
Magnetic Input Devices
- Magnetic Stripe Reader
Screen Input Devices
- Touch Screen
- Light Pen
- Mouse
Analog Input Devices
Output Devices
Card Puncher, Paper Tape Puncher
CRT
Printer (Impact, Ink Jet,
Laser, Dot Matrix)
Plotter
Analog
Voice
Peripheral Devices

## Slide 4: Input Output Interface
Designing logic circuits (Hardware) and writing instructions (Software) to enable the processor to communicate with peripherals is called interfacing, and the logic circuits are called I/O ports or interfacing devices.
I/O system and I/O module or I/O interface
Each device also has an individual controller that supervises the operation of the particular mechanism in the peripheral

## Slide 5: A Single Bus System

## Slide 6: Generic Model of I/O Module

## Slide 7: INPUT/OUTPUT INTERFACE
Input/Output Interfaces
Provides a method for transferring information between internal storage (such as memory and CPU registers) and external I/O devices
Resolves the differences between the computer and peripheral devices
  Peripherals – Electromechanical/Electromagnetic Devices
  CPU or Memory - Electronic Device
      Conversion of signal values required
  Data Transfer Rate
    Peripherals - Usually slower
    CPU or Memory - Usually faster than peripherals
      Some kinds of Synchronization mechanism may be needed
  Unit of Information
    Peripherals – Byte, Block, …
    CPU or Memory – Word
  Data representations and operating modes may differ

## Slide 9: Device Interface