## Slide 1
Dr. Rizwan Khan
Head – Department of Computer Science and Engineering
(An NBA Accredited Program)
ABES Institute of Technology, Ghaziabad
COMPUTER ORGANIZATION AND ARCHITECTURE

## Slide 2: I/O BUS AND INTERFACE MODULES
Input/Output Interfaces
The I/O modules take care of moving data between main memory and a particular device interface. Interfaces are designed specifically to communicate with certain types of devices, such as keyboards, disks, or printers. Interfaces handle the details of making sure that devices are ready for the next batch of data, or that the host is ready to receive the next batch of data coming in from the peripheral device.

## Slide 3: I/O MODULE
Interfaces
  Internal Interface to the CPU and memory via the system Bus
  External Interface to one or more I/O devices by tailored data links.
Requirements
  Control & Timing
    To coordinate the flow of traffic between internal resources and external devices
  CPU Communication
    Control signal to the I/O module over the control bus
    Exchange of data between CPU and I/O module over data bus
    Status signals like BUSY, READY needed as the data transfer rates of the CPU and the peripherals vary
    Address of the various peripherals connected to CPU
  Device Communication
    Commands, status information and data
  Data Buffering
  Error Detection

## Slide 5: I/O BUS AND MEMORY BUS
  * MEMORY BUS is for information transfers between CPU and the MM
  * I/O BUS is for information transfers between CPU
  and I/O devices through their I/O interface
  * Many computers use a common single bus system
  for both memory and I/O interface units
  - Use one common bus but separate control lines for each function
  - Use one common bus with common control lines for both functions
  * Some computer systems use two separate buses,
  one to communicate with memory and the other with I/O interfaces
Functions of Buses
Physical Organizations
Input/Output Interfaces